## Slide 1: EE351 微机原理与微系统
姜俊敏
电子与电子工程系

## Slide 2: 第六章 存储器
本章学习目标
Types of Memory
  Volatile Memory (RAM)
  Non Volatile Memory (ROM, Flash)
Larger/Wider Memories
Memory Interfacing (Decoding)
  Full Address Decoding
  Partial Address Decoding
  Block Address Decoding

## Slide 3: Topics
Types of Memory
  Volatile Memory (RAM)
  Non Volatile Memory (ROM, Flash)
Larger/Wider Memories
Memory Interfacing (Decoding)
  Full Address Decoding
  Partial Address Decoding
  Block Address Decoding

## Slide 4: Resources
  1 Objectives
  2 Internal Resource Mapping
  3 The Flash Memory Operation
  4 EEPROM
  5 External Memory Expansion

## Slide 5
68HC812A4 Block Diagram
CPU12
1-KB SRAM
4-KB EEPROM
I/O Ports
I/O Ports
Port T
Timer Module
Port AD
Analog to Digital
Port S
Serial
Communication
Interrupts

## Slide 6: CPU ­ Memory Interface
CPU ­ Memory Interface usually consists of:
  uni­directional address bus
  bi­directional data bus
  read control line
  write control line
  ready control line
  size (byte, word) control line
Memory access involves a memory bus transaction
  read:
    set address, read control signal and size signal,
    copy data when ready is set by memory
  write:
    set address, data, write control signal and size,
    done when ready is set
address bus
data bus
CPU
Memory
Read
Write
Ready
size

## Slide 7: Memory Hierarchy
The design constraints on a computer memory can be summed up by three questions (i) How Much (ii) How Fast (iii) How expensive.
There is a tradeoff among the three key characteristics
A variety of technologies are used to implement memory system
Dilemma facing designer is clear  large capacity, fast, low cost!!
Solution  Employ memory hierarchy
registers
Cache
Main Memory
Disk Cache
Magnetic Disk
Removable Media
Cost
Capacity
Access
Time

## Slide 8
CPU
Cache
Controller
Cache
Memory
PCI
Controller
DRAM
EISA/PCI Bridge
Controller
Hard Drive
Controller
Video
Adaptor
PC Card 1
PC Card 2
SCSI
Adaptor
PC Card 3
Local CPU / Memory Bus
Peripheral Component Interconnect Bus
EISA PC Bus
SCSI
Bus
Co-processor
Memory
Static RAM
Dynamic RAM
Registers

## Slide 9: Memory Classification:

## Slide 10: Classifications: Key Design Metrics

## Slide 11: Memory Roadmap

## Slide 12: Memory Roadmap

## Slide 13: RAM versus ROM
RAM
  Read/write
  Volatile
  Faster access time
  Variants
    SRAM
    DRAM
  Application
    Variables
    Dynamic memory allocation
    Heaps, stacks
ROM
  Read only
  Non-Volatile
  Slower
  Variants
    PROM,EPROM
    EEPROM, FLASH
  Application
    Programs
    Constants
    Codes, e.t.c

## Slide 14: Memory Technologies
DRAM: Dynamic Random Access Memory
  upside: very dense (1 transistor/capacitor per bit) and inexpensive
  downside: requires refresh and often not the fastest access times
  often used for main memories
SRAM: Static Random Access Memory
  upside: fast and no refresh required
  downside: not so dense (6 transistors per cell) and not so cheap
  often used for caches
ROM: Read­Only Memory (Flash, EPROM, EEPROM)
  Upside: nonvolatile
  Downside: Slow to write to
  often used for bootstrapping, implementing functions (SQRT)

## Slide 15: Static RAM

## Slide 16: 16 X 1 RAM
4 address lines required to access 16 locations.
A Decoder is added to select the different words (each 1 bit wide).
For 16 words we need a 4-to-16 line Decoder

## Slide 17: Row/Column
Practical memories contains thousands of words!!
If RAM gets large, there is a huge decoder
Also run into chip layout issues
How can we change the structure of Memory to solve this problem?
  Rearrange the memory into “2D” i.e., matrix layout

## Slide 18: 16 X 1 as 4 X 4 Array
Two decoders
  Row
  Column
Address just broken up
Not visible from outside

## Slide 19: MCM6264C 8K x 8 Static RAM

## Slide 20: SRAM Memory Timing for Read Accesses

## Slide 21: SRAM Memory Timing for Write Accesses

## Slide 22: DRAM Organization and Operations
In the traditional DRAM, any storage location can be randomly accessed for read/write by inputting the address of the corresponding storage location.
  Memory cell consists of a transistor and a capacitor. The charge on the capacitor represents 0 or 1 for the memory cell. The support circuitry for the DRAM chip is used to read/write to a memory cell.
  A typical DRAM of bit capacity 2N * 2M consists of an array of memory cells arranged in 2N rows (word-lines) and 2M columns (bit-lines).
  Each memory cell has a unique location represented by the intersection of word and bit line.

## Slide 23: DRAM Cell

## Slide 24: Memory Array Architecture

## Slide 25: Symbolic Representation of DRAM
To write data:
  Signals from address decoding R/W logic will close switches S1, S2 while keeping S3,S4 open
  So input data is connected to C then switches (S1, S2) are disconnected.
To read data:
  Switches S2,S3,S4 are closed while S1 is open
  This connects stored capacitor voltage to sense amplifier
  The sense amplifier will compare the capacitor voltage to a reference voltage and produce a solid ‘0’ or ‘1’ and C gets refreshed.

## Slide 26: DRAM Characteristics
Destructive Read
  When cell read, charge removed
  Must be restored after a read
Refresh
  Also, there’s steady leakage
  Charge must be restored periodically
DRAM are dense (lots of cells) so there are many address lines.
  To reduce the physical size of DRAM we can reduce the number of pins by applying the address lines serially in to parts (Row Address and then Column Address)

## Slide 27: Address Multiplexing
27
16K x 1 DRAM  14 address lines
64K x 1 DRAM  16 address lines
4M x 1 DRAM  22 address lines
High capacity memory chips require many pins if each address required a separate pin
Solution: In order to reduce # of pins on DRAM chips manufacturers utilize address multiplexing  whereby each address input pin can accommodate two different address bits.
What does this translate to?
  Significant decrease in size of IC package
  Better yield
  Maximize the amount of memory that can fit on one board
  Cheaper ICs

## Slide 28: DRAM Memory Access
DRAM Memory is arranged in a XY grid pattern of rows and columns.
  First, the row address is sent to the memory chip and latched,
  then the column address is sent in a similar fashion.
This row and column-addressing scheme (called multiplexing) allows a large memory address to use fewer pins.
The charge stored in the chosen memory cell is amplified using the sense amplifier and then routed to the output pin.
Read/Write is controlled using the read/write logic.

## Slide 29: How DRAM Works
A7A6A5A4
A3A2A1A0
A7A6A5A4A3A2A1A0

## Slide 30: DRAM Logical Diagram

## Slide 31: DRAM `Read’ Timing Waveform
After Applying RAS and CAS the output enable is applied to access the data
Delay until data available

## Slide 32: DRAM `Write’ Timing

## Slide 33: DRAM Types: Synchronous vs. Asynchrnous
DRAM - Dynamic RAM
FPM DRAM - Fast page-mode RAM
EDO DRAM - Extended Data Out RAM
BEDO DRAM - Burst Extended-data-out RAM
SDRAM - Synchronous Dynamic RAM
DDRRAM - Double Data Rate RAM
DDR2 (Twice the speed of DDR SDRAM)
DDR3 (Twice the speed of DDR2 SDRAM)
DDR4 (In Production ??)

## Slide 34: Page Mode DRAM
DRAMs made to read & write blocks
Example
  Assert RAS, leave asserted
  Assert CAS multiple times to read sequence of data
Similar for writes

## Slide 35: DRAM Evolution (Synchronous)
There has been multiple improvements to the DRAM design in the past 10 years.
  A Clock signal was added making the design synchronous (SDRAM).
  The data bus transfers data on both rising and falling edge of the clock (DDR SDRAM)
  Second generation of DDR memory (DDR2) scales to higher clock frequencies.
  Third generation (DDR3) has lower power consumption, higher clock frequency and denser modules

## Slide 36: Synchronous DRAM (SDRAM)
Double Data Rate SDRAM
Transfers data on both edges of the clock

## Slide 37: Larger/Wider Memories
Made up from sets of chips
Consider a 64K by 8 RAM
How to design a 256K x 8 RAM using a 64K ?
How many address lines in total?

## Slide 38: Larger Memory
256K X 8
Connect all output data lines together (tristate)
Connect all input data line together
16 lines of address to fetch a word in any DRAM chip
How to select the specific DRAM chip?

## Slide 39: Larger Memory
Decoder for high-order 2 bits
  Selects chip
  Look at selection logic
  Address ranges

## Slide 40: Wider Memory – 64K X 16

## Slide 41: Read Only Memory

## Slide 42
Mask-Programmed Devices
The entire ROM consists of a number of row (word) and column (data) lines forming an array.
Each column has a single pull-up resistor attempting to hold that column to a weak logic 1 value.
Every row-column intersection has an associated transistor and, potentially, a mask-programmed connection.

## Slide 43
Fusible-Link Based PROM (OTP)
The problem with mask-programmed devices is that creating them is a very expensive unless you intend to produce them in large quantities.
For this reason, the first programmable read-only memory (PROM) devices were developed at Harris Semiconductor in 1970.

## Slide 44: EPROM Technology
PROM: Programmable ROM
  It can be programmed (written to) only once via a PROM programmer
EPROM: Erasable Programmable ROM
  The first device – the 1702 – introduced by Intel in 1971.
  It can be erased with an ultraviolet light and then rewritten via a EPROM programmer

## Slide 45
Standard MOS vs. EPROM Transistor
An EPROM transistor has the same basic structure as a standard MOS transistor, but with the addition of a second polysilicon floating gate isolated by layers of oxide.

## Slide 46: Non-Volatile Memories The Floating-gate transistor (FAMOS)
Floating gate
Source
Substrate
Gate
Drain
n
+
n
+_
p
t
ox
t
ox
Device cross-section
Schematic symbol
G
S
D

## Slide 47: EPROM Cell: Floating Gate Transistor

## Slide 48: EPROM Cell: Floating Gate Transistor
Ids
Vgs
Vt is pushed from 0.7 volts towards 5-7 Volts. So transistor will be off unless it is reprogrammed again.

## Slide 49: EPROM Cell: Programming/Erasing
Programming: apply a high voltage typically (10V – 25V) for a specified amount of time (typically 50 ms per address) and this requires a special programming circuit.
  This will usually trap electrons in floating gate and program the bit to a ‘0’ value.
Erasing: expose the EPROM to UV light, this will force the electrons trapped (due to application of high voltage) back to silicon substrate.
  This will usually take 15-20 minutes
  It will erase the entire chip

## Slide 50
EPROM Transistor-based Memory Cell
In its un-programmed state, all the floating gates in the EPROM transistors are uncharged.
In this case, placing a row line in its active state will turn on all of the transistors and column lines are pulled to logic “0”.

## Slide 51
EPROM Transistor-based Memory Cell
As they are order of magnitude smaller than fusible links, EPROM cells are efficient in terms of silicon real estate.
An EPROM device is delivered in a ceramic or plastic package with a small quartz window in the top.
The main problem with EPROM devices are
  Their expensive packages with quartz window and
  The time it takes to erase them, which is in the order of 20 minutes.
  To program the device or erase it, a programmer has to remove the device from the host circuit board and put onto a special programming device.
  As the structures on the device become smaller and the density increases, a larger percentage of the surface of the die is covered by metal. This make it difficult for the EPROM cells to absorb the UV light and increases the required exposure time.

## Slide 52: EEPROM
EEPROM (Electrically Erasable PROM) overcomes the limitations of the PROM by electrically programming and erasing the chip onboard.
The structure looks similar to the floating gate EPROM (FAMOS transistor, floating gate avalanche transistor) with some minor modifications (FLOTOX Transistor)  the insulating oxide layers surrounding this gate are very much thinner.
  Programming: involves applying a high voltage
  Erasing: involves applying a reverse high voltage which causes a removal of trapped charge (tunneling)

## Slide 53: FLOTOX EEPROM
Floating gate
Source
Substrate
p
Gate
Drain
n
1
n
1
FLOTOX transistor
Fowler-Nordheim
20
–
30 nm
10 nm

## Slide 54: EEPROM Cell
WL
BL
V
DD
 2 transistor cell
A second transistor is used to select cell for erasure.
  Advantages: electrically erase bytes in circuit
  Disadvantages: less dense than EPROM

## Slide 55: FLASH (NAND vs. NOR)
The FLASH traces its ancestry to both the EPROM and EEPROM technologies (introduced in 1984/1988)
The name “FLASH” was originally coined to reflect this technology’s rapid erasure times compared to EPROM.
FLASH employs a variety of architectures.
  Some have a single floating gate transistor cell with the same area as an EPROM cell, but with the thinner oxide layers characteristic of an EEPROM.
    These devices can be electrically erased, but only by clearing the whole device or large portions.
  Other architectures features a two-transistor cell similar to that of an EEPROM cell, thereby allowing them to be erased and reprogrammed on a word-by-word basis.

## Slide 56: Flash EEPROM
Control gate
erasure
p-
substrate
Floating gate
Thin tunneling oxide
n
1
source
n
1
drain
programming
Many other options …

## Slide 57: Flash EEPROM

## Slide 58: Interacting with Flash and E2PROM

## Slide 59: Flash EEPROM: NAND vs. NOR

## Slide 60: Flash EEPROM

## Slide 61: Flash EEPROM: SLC vs. MLC
Single-level (SLC) NAND stores two states per memory cell and enables one bit programmed/read per memory cell.
Multi-level cell NAND (MLC) stores four states per memory cell and enables two bits programmed/read per memory cell.

## Slide 62: Flash EEPROM: SLC vs. MLC

## Slide 63: Flash EEPROM: Further

## Slide 64: Flash EEPROM: Further

## Slide 65: Flash EEPROM: Further
Micron’s proprietary CMOS-under-Array technique constructs the multilayered stack over the chip’s logic, packing more memory into a tighter space and shrinking 176-layer NAND’s die size, yielding more gigabytes per wafer.

## Slide 66: Flash EEPROM: Further
目前，NAND SSD 主要有两种结构设计，一种是英特尔 Floating Gate，另一种是 Charge Trap。这两种设计在结构上有很大不同。比如在上图中，FloatingGate 是浅蓝色部分，黄色部分是绝缘体，通过隧道效应把电子俘获到蓝色的部分当中。在 Floating Gate 技术架构下，每一层之间是断开的，而在 Charge Trap 当中，上下是靠中间的绝缘体把电荷俘获在那里，默认电子进去之后不会逃逸。在层数有限的情况下，Charge Trap 架构是可行的，当堆叠过多时，电子逃逸情况就无法保证。

## Slide 67: Flash EEPROM: SLC vs. MLC

## Slide 68: Flash EEPROM

## Slide 69: Latency of FLASH SSD
Reference: https://www.firstxw.com/view/243774.html

## Slide 70: Major Markets Driving Flash
The Figure below shows how demand for NAND Flash has been driven primarily by several major markets – solid state drives, mobile phones, Flash memory cards, USB Flash drives and MP3 Players.

## Slide 71: Memory: Comparison
Memory type | Density | Speed | Size | Cost | Volatility
DRAM | V.High | Slow | Small | V. Cheap | Y
SRAM | Low | V. fast | Large | Costly | Y
ROM | High | fast | Small | Cheap | N
PROM | High | fast | moderate | Cheap | N
EPROM | High | V. Slow | Small | Cheap | N
EEPROM | Medium | V. Slow | Moderate | Cheap | N
Flash | High | V. Slow | Small | Cheap | N

## Slide 72: Address Decoding: Basic Concept
HC12
To transfer data correctly and protect the computer from damaging, only one device at a time should be allowed to drive the data bus. The address decoder selects and enables one and only one data transfer device at a time.

## Slide 73: Address Decoding: When Needed
73
Address decoding is the task of designing decoding circuitry when mapping memory to different memory locations.
  Required for a microcomputer where memory and I/O support are essential
  Needed for embedded system when on chip microcontroller memory is not sufficient

## Slide 74: Address Decoding: Techniques
Several techniques exist to perform address decoding
  Full Address Decoding
  Partial Address Decoding
  Block Address Decoding
Each technique has advantages/disadvantages:
  Cost
  Speed
  Simplicity
  Future Expansion

## Slide 75: Example : Full Address Decoding
Data bus
SRAM1: $2000 - $3FFF
ROM1: $4000 - $5FFF
EEPROM: $6000 - $7FFF
SRAM2: $A000 - $BFFF
ROM2: $C000 - $DFFF
HC12
Address bus
SRAM1
SRAM2
ROM1
ROM2
EEPROM
Control bus
Address decoding circuit
As the name implies you will use all the address lines to construct the decoding circuitry.

## Slide 76: Designing Address Decoders
A designer can implement the address decoding techniques in several ways:
  Random Logic
  M-line to n-line decoders
  PROMS & Programmable logic
Random Logic:
  Advantages: Speed i.e. it can use the fastest logic available
  Disadvantages: Requires high chip count and lacks flexibility.
Decoders: Most widely used
  Examples:
    74LS138 (3-to-8 line decoder)
    74LS139 (dual 2-line to-4-line decoder)
    74LS154 (4-to-16 line decoder)
  Advantage: modular, and flexible
  Disadvantage: Slower, waste of some logic

## Slide 77: Full Address Decoding: Example
Design a fully decoded positive logic select signal for 1K RAM located at $4000 - $43FF, with a processor having 16 address lines
Step #1  Write specified address using 0,1,X
  There are 16 symbols, one for each bit A15 – A0
  “0”  address bit must be 0 for this device
  “1”  address bit must be 1 for this device
  “X”  address bit can be either 0 or 1
    All X’s are located on the RHS
    Let “n” be the number of X’s, where size of memory in bytes is 2n
  Let “I” be unsigned binary integer formed from 16 – n (0’s and 1’s)
    I = Start Address/Memory Size
  In our example:
    n = 10, size = $0400 = 1K
    I = StartAddress/MemorySize = $4000/$0400 = (010000)2 = (16)10
    Address  010000XXXXXXXXXX

## Slide 78: Full Address Decoding
Step #2  Write the equations using all 0’s and 1’s
  A “0” translates into the complement of the address bit
  A “1” translates directly into the address bit
  The address  0 1 0 0 0 0 X X X X X X X X X X
  A15.A14.A13.A12.A11.A10
Step #3  Build the circuit using logic
  This is used for the chip select of the IC.
Observations: 010000XXXXXXXXXX
  If we set all the Xs to 0, we get the starting address
  If we set all the Xs to 1, we get the ending address
  Common Error: If all Xs are not in a group on the RHS, then the address range will become discontinuous
Use full-address decoding on systems where future expansion is likely

## Slide 79: Assigning Addresses
Suppose we are given:
  10K bytes of ROM as one 2K block (called ROM1)
  8K block (called ROM2)
  2K bytes of RAM (called RAM)
  2 bytes for peripheral 1 (called PERI1)
  2 bytes for peripheral 2 (called PERI2)
  But arranged as:
    00 0000 - 00 07FF ROM1  2K (11 lines X)
    00 0800 - 00 0FFF RAM  2K (11 lines X)
    00 4000 - 00 5FFF ROM2  8K (13 lines X)
    00 8000 - 00 8001 PERI1  2 Bytes (1 line X)
    00 8002 - 00 8003 PERI2  2 Bytes (1 line X)
THE PROCESSOR HAS 24 ADDRESS LINES

## Slide 80: Assigning Addresses (Cont’d)
  00 0000 - 00 07FF ROM1  2K (11 lines X)
  00 0800 - 00 0FFF RAM  2K (11 lines X)
  00 4000 - 00 5FFF ROM2  8K (13 lines X)
  00 8000 - 00 8001 PERI1  2 Bytes (1 line X)
  00 8002 - 00 8003 PERI2  2 Bytes (1 line X)
ADDRESS LINE
Device 23 22 21 20 ... 15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00
ROM1 0 0 0 0 ... 0 0 0 0 0 x x x x x x x x x x x
RAM 0 0 0 0 ... 0 0 0 0 1 x x x x x x x x x x x
ROM2 0 0 0 0 ... 0 1 0 x x x x x x x x x x x x x
PERI1 0 0 0 0 ... 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 x
PERI2 0 0 0 0 ... 1 0 0 0 0 0 0 0 0 0 0 0 0 0 1 x
Equation for ROM1  A23A22A21A20A19A18A17A16A15A14A13A12A11

## Slide 81: Full Address Decoding Network
ROM1 Select
A11
A12
A13
A14
A23

## Slide 82: II Partial Address Decoding
Product information: 2KB (211) external EEPROM and 2KB external SRAM
Data bus
HC12
Address bus
SRAM
EEPROM
Control bus
The lowest 11 address bits are connected directly to the memory devices address pins
The highest 5 bits are available for address decoder
However, we don’t need to use all 5 bits.
The example only uses 2 bits: A15 and A14
74LS139 is used (2-to-4 decoder)
Why is this “partial address decoding”?
Advantages? Disadvantages?

## Slide 83: Assigning Addresses
Suppose we are given:
  8K bytes of RAM
  8K block of EEPROM
Design a partial address decoder to connect the RAM and EEPROM to a 20 bit address line.

## Slide 84: Partial Address Decoding

## Slide 85: Partial Address Decoding
Partial address decoding is so called because not all address lines available for address decoding take part in the decoding process.
It is the simplest and least expensive form to implement.
Partial address decoding was very popular in the early days of the 8-bit microprocessor and is still found in small dedicated systems were low cost is of paramount importance.
However the main drawback is that it prevents the full use of the micro-processor available memory and makes it difficult to expand the memory system

## Slide 86: Repeat with Partial Address Decoding
Suppose we are given:
  10K bytes of ROM as one 2K block (called ROM1)
  8K block (called ROM2)
  2K bytes of RAM (called RAM)
  2 bytes for peripheral 1 (called PERI1)
  2 bytes for peripheral 2 (called PERI2)
but arranged as:
  00 0000 - 00 07FF ROM1  2K (11 lines X)
  00 0800 - 00 0FFF RAM  2K (11 lines X)
  00 4000 - 00 5FFF ROM2  8K (13 lines X)
  00 8000 - 00 8001 PERI1  2 Bytes (1 line X)
  00 8002 - 00 8003 PERI2  2 Bytes (1 line X)

## Slide 87: Partial Address Decoding: Address Table
ADDRESS LINE
Device 23 22 21 20 ... 15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00
ROM1 0 0 0 ... x x x x x x x x x x x
RAM 0 0 1 ... x x x x x x x x x x x
ROM2 0 1 ... x x x x x x x x x x x x x
PERI1 1 0 ... x
PERI2 1 1 ... x
For this table, no further memory devices can be added!!
The existing memory devices fill the entire 8M words of
memory space.

## Slide 88: Partial Address Decoding: Implementation
A23
A22
A21
CS_ROM1#
CS_RAM#
CS_ROM2#
CS_PERI1#
CS_PERI2#

## Slide 89: Example 2: Partial Address Decoding
Design four minimal-cost select signals in positive logic:
  4K RAM $0000 to $0FFF
  Input $5000
  Output $5001
  16K ROM $C000 to $FFFF
Solution:
  Step #1, Write the addresses in binary
    RAM 0000, XXXX, XXXX, XXXX
    Input 0101, 0000, 0000, 0000
    Output 0101, 0000, 0000, 0001
    ROM 11XX, XXXX, XXXX, XXXX

## Slide 90: Cont .. Partial Address Decoding
  Step #2, Choose as many address lines that are required to differentiate between the devices (Consider the different devices in pair wise fashion). In this example choose A15, A14, A0.
  Step #3: Draw a Karnaugh map for each device
    Put a true for addresses specified by that device
    Put a false for other devices
    Put an “X” for unspecified addresses.

## Slide 91: Minimal Cost Address Decoding
RAM
ROM
Input
Output
A15 A14
A15 A14
A15 A14
A15 A14
A0
A0
A0
A0
00
01
00
10
11
01
00
10
11
01
00
11
10
01
11
10
0
1
0
0
0
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
X
X
X
X
X
X
X
X
  RAM 0000, XXXX, XXXX, XXXX
  Might lead to Conflict!

## Slide 92: Partial Address Decoding
Use minimal-cost decoding (i.e. Partial) on systems where cost and speed are more important than future expansion.
  If one does not select enough address lines to differentiate between the devices, then some addresses may incorrectly select more than one device.
  If one selects too many address lines, then the KMAP will be harder to draw, but the resulting solution should be the same.

## Slide 93
93
Cheaper
A15 A14
A0
00
01
11
10
0
1
Ram
X
X
Minimal Cost Decoding: Alternatives
Ram
In
Out
Rom
Rom
Ram
Ram
Ram
Ram
In
In
Out
Out
Rom
Rom
Rom
Rom
X
X
X
X
A0
A0
A15 A14
A15 A14
Safer
Expandable
Notes: 93

## Slide 94: Block Address Decoding
Is a compromise between partial and full address decoding
  Divide the memory space into a number of fully decoded blocks, generally of equal size
  The method then uses high-order bits of address to select the block and the low-order bits to select the sub-block

## Slide 95: Block Address Decoding
95
Say we want to split the 68000 processor address space into 512 KB blocks (Block address decoding)
  How many blocks are there?
    16 MB / 512 KB = 32 (224 / 219 = 25)
  How many bits do we need to differentiate between blocks?
    5 bits
  How many bits do we need to decode to choose locations within each block?
    “19” bits
Notes: 95

## Slide 96: Summary
Memories are considered to be an important component of any embedded system.
Designers have to make a crucial decision among all the memory technologies that are available in terms of (a) Cost (b) Speed (c) ease of use (d) …
Adding memory or peripheral memory-mapped devices to a microcontroller involves three issues:
  Memory space assignment
  Address decoder and control circuitry design
  Timing Verification
Techniques to perform address decoding
  Full Address Decoding (Efficient)
  Partial Address Decoding (Cheap, Simple)
  Block Address Decoding (Compromise)

## Slide 97: ROM: Masked Programmed
97
Memory that is permanent
k address lines
2k items
n bits

## Slide 98: Memory Subsystem Components
Memory subsystems generally consist of chips+controller
Each chip provides few bits (e.g., 1­4) per access
  Bits from multiple chips are accessed in parallel to fetch bytes and words
  Memory controller decodes/translates address and control signals
  Controller can also be on memory chip
address bus
data bus
CPU
Memory
Read
Write
Ready
Size
1-of-16
decoder
1 0 1 1 0 0 1 0
1 0 0 0 0 0 0 1
0 1 0 1 0 0 1 1
address
0000
0001
1111
16x1-bit memory chip
16x8-bit memory array
D7 D6 D5 D4 D3 D2 D1 D0

## Slide 99: Interacting with a Memory Device

## Slide 100: DRAM Organization and Operations
Address decoders
  to select a row and a column
(b) Sense amps
  to detect and amplify the charge in the capacitor of the memory cell.
(c) Read/Write logic
  to read/store information in the memory cell.
(d) Output Enable logic
  controls whether data should appear at the outputs.
(e) Refresh counters
  to keep track of refresh sequence.

## Slide 101: Timing: 4M x 4 DRAM
Say need to refresh every 64ms
Distributed refresh
  Spread refresh out evenly over 64ms
  On a 4Mx4 DRAM  4096 rows
  Refresh every 64ms/4096=15.6 us
  Total time spent is 0.25ms, but spread
Burst refresh
  Same 0.25ms, but all at once
  May not be good in a computer system
Refresh takes low % of total time

## Slide 102: Static Column Mode DRAM
Looks like Page Mode DRAM except that CAS is not cycled after first column access
Example
  Assert RAS, leave asserted
  Assert CAS, leave asserted
  Provide new column address
Similar for writes

## Slide 103: DRAM Performance Specs
Important DRAM Performance Considerations
  Random access time: time required to read any random single cell
  Fast Page Cycle time: time required for page mode access ­­ read/write to memory location on the most recently­accessed page (no need to repeat RAS in this case)
  Extended Data Out (EDO): allows setup of next address while current data access is maintained
  SDRAM ­ Burst Mode: Synchronous DRAMs use a self­incrementing counter and a mode register to determine the column address sequence after the first memory location accessed on a page ­­ effective for applications that usually require streams of data from one or more pages on the DRAM
  Required refresh rate: minimum rate of refreshes

## Slide 104: Synchronous DRAM (SDRAM)
Has a clock
Common type in PCs late-90s
Multiple banks
Pipelined
  Start read in one bank after another
  Come back and read the resulting values one after another

## Slide 105: Notional View of Internals

## Slide 106: Programmed Truth Table

## Slide 107: Resulting Programming

## Slide 108: 74138 & 74139 decoder
74138
O0
O1
O2
O3
O4
O5
O6
O7
E1
E2
E3
A2
A1
A0
74139
1Y0
E1
A1
A0
E2
B1
B0
1Y1
1Y2
1Y3
2Y0
2Y1
2Y2
2Y3
3-to-8 decoder
2-to-4 decoder
Internal structure?

## Slide 109: Addressing with Memory Map

## Slide 110: EPROM, EEPROM, Flash
Device | EPROM | Flash | EEPROM
Cell Size | 1.0 | 1.0-1.2 | 3.0
Programming | Hot Electron Injection | Hot Electron Injection | Tunneling
Erase Technique | UV Light | Tunneling | Tunneling
Erase Time | 20 Min | 1 S | 5 ms
Min Erase | Entire Chip | Sectors | Byte
Write Time (64B) | > 100 usec | > 500 usec | > 700 usec
Read Time | 4.5 us | 4.5 us | 4.5 us

## Slide 111: Addressing with Memory Map

## Slide 112: Addressing with Memory Map

## Slide 113: Partial Address Decoding

## Slide 114: Storage Basics
Just because the CPU sees RAM as one long, thin line of bytes doesn't mean that it's actually laid out that way
Real RAM chips don't store whole bytes, but rather they store individual bits in a grid, which you can address one bit at a time

## Slide 115: DRAM Memory Access
Hardware Diagram of
Typical DRAM (2 N x 2N x 1)
A typical DRAM read operation:
1. The row address is placed on the address pins via the address bus
2. RAS pin is activated, which places the row address onto the Row Address Latch.
  The Row Address Decoder selects the proper row to be sent to the sense amps.
  The Write Enable is deactivated, so the DRAM knows that it’s not being written to.
  The column address is placed on the address pins via the address bus
6. The CAS pin is activated, which places the column address on the Column Address Latch
7. The CAS pin also serves as the Output Enable, so once the CAS signal has stabilized, the sense amps place the data from the selected row and column on the Data Out pin so that it can travel the data bus back out into the system.
8. RAS and CAS are both deactivated so that the cycle can begin again.

## Slide 116: DRAM Refresh
Many strategies
Logic on chip
Refresh counter and Refresh controller
Refresh counter is used to provide the address of the row of DRAM cell to be refreshed.

## Slide 117: CAS Before RAS
Set column address
Apply CAS first (opposite of RW)
Then toggle RAS enough times to cycle through row addresses
On-board refresh counter applies the row addresses
CAS
RAS
Col Add
Row Add
Row Add
Row Add
Row Add

## Slide 118: NAND Flash Memory
Unit Cell
Word line(poly)
Source line
(Diff. Layer)

## Slide 119: Basic Operations in a NOR Flash Memory―Erase

## Slide 120: Basic Operations in a NOR Flash Memory―Write

## Slide 121: Basic Operations in a NOR Flash Memory―Read

## Slide 122: NAND flash memory
Structure of NAND flash memory.
The main characteristic of NAND flash memory is that it does not support in-place updates.